## Slide 1: SMB University: Cisco SMB Foundation Solutions
Networking Fundamentals

## Slide 2: Objectives
Describe the function and operation of a hub, a switch and a router
Describe the function and operation of a firewall and a gateway
Describe the function and operation of Layer 2 switching, Layer 3 switching, and routing
Identify the layers of the OSI model
Describe the functionality of LAN, MAN, and WAN networks
Identify the possible media types for LAN and WAN connections

## Slide 3: What is a Network?
A network refers to two or more connected computers that can share resources such as data, a printer, an Internet connection, applications, or a combination of these resources.

## Slide 4: Types of Networks
Local Area Network (LAN)
Metropolitan Area Network (MAN)
Wide Area Network (WAN)

## Slide 5: WAN Technologies
Circuit-switched
Asynchronous serial. ISDN Layer 1
TELEPHONE COMPANY
Leased Line
Synchronous serial

## Slide 6: WAN Technologies (Cont.)
Broadband Access
SERVICE PROVIDER
Cable, DSL, Wireless WAN
Frame-Relay
Synchronous serial
SERVICE PROVIDER

## Slide 7: Network Topologies: Bus Topology
SEGMENT
Terminator
Terminator

## Slide 8: Network Topologies: Star Topology
Hub

## Slide 9: Network Topologies: Extended Star Topology

## Slide 10
7
6
5
4
3
2
1
The OSI Model—
Why a Layered Network Model?
Reduces complexity
Standardizes interfaces
Facilitates modular engineering
Ensures interoperable technology
Accelerates evolution
Simplifies teaching and learning
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 11: The Seven Layers of the OSI Model
Application Layers (Upper Layers):
Network Processes to Applications
Data Representation
InterHost Communication
7
6
5
4
3
2
1
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 12: The Seven Layers of the OSI Model (Cont.)
7
6
5
4
3
2
1
Application
Presentation
Session
Transport
Network
Data Link
Physical
End To End Connections:
Handles transportation issues between hosts
Ensures data transport reliability
Establishes, maintains and terminates virtual circuits
Provides reliability through fault detection and recovery
Information flow control

## Slide 13: The Seven Layers of the OSI Model (Cont.)
7
6
5
4
3
2
1
Application
Presentation
Session
Transport
Network
Data Link
Physical
Data Delivery:
Provides connectivity and path selection between two host systems
Routes data packets
Selects best path to deliver data
The Network layer prioritizes data known as Quality of Service (QoS)

## Slide 14: The Seven Layers of the OSI Model (Cont.)
7
6
5
4
3
2
1
Application
Presentation
Session
Transport
Network
Data Link
Physical
Access to Media:
Defines how data is formatted for transmission and how access to the network is controlled

## Slide 15: The Seven Layers of the OSI Model (Cont.)
7
6
5
4
3
2
1
Application
Presentation
Session
Transport
Network
Data Link
Physical
Binary Transmission:
Defines the electrical, mechanical, procedural, and functional specifications for activating, maintaining, and deactivating the physical link

## Slide 16: Physical Media Types
Twisted-Pair
Coaxial
Outer jacket
BNC
Connector
Copper Conductor
Braided Copper Shielding
Plastic Insulation
Fiber Optics
Outer jacket
Plastic Shield
Glass and Fiber Cladding
Kevlar Reinforcing Material
SC
Connector
Outer jacket
Twisted-Pair
Color-Coded Plastic Insulation
RJ-45
Connector

## Slide 17: Physical Media Types (Cont.)
Wireless
INTERNET
ETHERNET BACKBONE

## Slide 18: Physical Media Comparison
 | Twisted Pair | Coaxial | Fiber Optic | Wireless LAN
Bandwidth | Up to 1 Gbps | 10–100 Mbps | Up to 10 Gbps or higher | Up to 54 Mbps
Distance | Up to 100 m | Up to 500 m | Up to 60 km | Up to 100 m
Price | Least expensive | Inexpensive | Most expensive | Moderate

## Slide 19: Hub or Repeater
A hub (concentrator) is a device that repeats the signals it receives on one port to all other ports. It is a central connection point for several network devices.
Hub

## Slide 20: Network Interface Card

## Slide 21: Hub (Multiport Repeater)

## Slide 22: WAN—Physical Layer Implementations
Physical layer implementations vary
Cable specifications define speed of link
Cisco HDLC | PPP | Frame Relay | ISDN BRI (with PPP) | DSL Modem | Cable Modem
EIA/TIA-232 |  |  | RJ-48 | RJ-11 | BNC
EIA/TIA-449 X.21 V.24 V.35 HSSI |  |  | Note: ISDN BRI cable pinouts are different than the pinouts for Ethernet. The RJ-48 and RJ-45 look the same, but the pinouts are different. | Note: Works over telephone line | Note: Works over Cable TV line

## Slide 23: Physical Media
WAN
Wall Jack

## Slide 24: Data Link Layer
Data Link layer protocols create, transmit, and receive packets. This layer is also responsible for logical MAC addressing and LLC processing, creating logical topologies, and controlling media access.
2
Data Link

## Slide 25: MAC Address
The network interface card address, called the hardware address, is protocol-independent and is usually assigned at the factory. This address is technically called the media access control address (MAC) because it is found on the MAC sub layer of the Data Link layer.
2
Data Link
MAC Address =
Hardware Address
00-0C-F1-5E-BE-F2

## Slide 26: Data Link Devices
The Data Link layer is manipulated by two devices: bridges and switches. These are more complex and more expensive than their Physical layer counterparts, but they do have advantages.
Switches
Bridges

## Slide 27: Switch
When a switch receives data the switch examines the data link header for the MAC address of the destination station and forwards it to the correct port. This opens a path between ports that can use the full bandwidth of the topology.

## Slide 28: Network Layer
The network layer provides connectivity and path selection between two host systems that may be located on geographically separated networks
3
Network

## Slide 29: Network Layer Devices
The devices that operate at the Network layer are routers and Layer 3 Switches
Router
Layer 3 Switch

## Slide 30: Network Layer (Cont.)
IP is a standard that defines the manner in which the network layers of two hosts interact. IP addresses are 32 bit long, hierarchical addressing scheme.
3
Network
IP Address
Logical Address
=
192.168.6.17

## Slide 31: Routers
Routers facilitate communication within this internet work. It decides how to send packets within the network so that they arrive at their destination.

## Slide 32: Layer 3 Switches
The Layer 3 switch functions at the Network layer and performs the multiport, virtual LAN, data pipelining functions of a standard Layer 2 switch. It can also perform basic routing functions between virtual LANs.
Layer 3 Switch

## Slide 33: Multilayer Switching
Combines functionality of:
  Layer 2 switching
  Layer 3 switching
  Layer 4 switching
High-speed scalability
Low latency compared to routers
2
1
Physical
7
6
5
4
Application
Presentation
Session
3
Data Link
Transport
Network

## Slide 34: Transport Layer Implementations
The Transport layer is charge of the reliable/unreliable transport of data. It can be implemented as TCP or UDP.
4
TCP
UDP
Transport

## Slide 35: Gateway
A gateway is a combination of hardware and software that connects dissimilar network environments. It performs translations at multiple layers of the open system interconnection (OSI) model.
PC Network
MAC Network
Gateway
OSI Model

## Slide 36: Firewalls
A firewall is a system or group of systems that manages access between two or more networks
Outside Network
Inside Network
INTERNET
DMZ
Network

## Slide 37: Summary
This lesson covered the following main topics:
The function and operation of a hub, a switch, and a router
The function and operation of Layer 2 switching, Layer 3 switching, and routing
The OSI model
Functionality of LAN, MAN and WAN networks
Possible media types for LAN and WAN connections
The function and definition of firewalls and gateways